## Slide 1: coco

## Slide 2: start
We propose a Capacity-Optimized Cooperative
(COCO) topology control scheme to improve the network capacity in MANETs by jointly optimizing transmission mode selection, relay node selection, and interference control in MANETs with cooperative communications.
Through simulations, we show that physical layer
cooperative communications have significant
impacts on the network capacity, and the proposed
topology control scheme can substantially
improve the network capacity in MANETs with
cooperative communications.

## Slide 3: Problem and solution
Problem:FOR improving the performance of information transmission operating over the ever-challenging wireless medium which cant be achieved by multiple transmit antennas .
Solution:Cooperative communication has emerged as a new dimension of diversity to emulate the strategies designed for multiple antenna systems, since a wireless mobile device may not be able to support multiple transmit antennas due to size, cost, or hardware limitations [1]. By exploiting the broadcast nature of the wireless channel, cooperative communication allows single-antenna radios to share their antennas to form a virtual antenna array, and offers significant performance enhancements.
Notes: 1. This promising technique has been considered in the IEEE 802.16j standard, and is expected to be integrated into Third Generation Partnership Project (3GPP) Long Term Evolution (LTE) multihop cellular networks [2].
2 =>Recent tremendous interests in cooperative communications are due to the increased understanding of the benefits of multiple antenna systems [1].
Although multiple-input multiple-output (MIMO) systems have been widely acknowledged, it is difficult for some wireless mobile devices to support
multiple antennas due to the size and cost constraints. Recent studies show that cooperative communications allow single-antenna devices to
work together to exploit the spatial diversity and reap the benefits of MIMO systems such as resistance to fading, high throughput, low transmitted
power, and resilient networks.

## Slide 4: Existing work
Existing work: cooperative communications, most existing works are focused on link-level physical layer issues,such as outage probability and outage capacity [3,4].
Consequently, the impacts of cooperative
communications on network-level upper layer
issues, such as topology control, routing and network capacity, are largely ignored

## Slide 5: Detail idea
How cooperation achieved?
In a simple cooperative wireless network model with two hops, there are a source, a destination, and several relay nodes. The basic idea of cooperative relaying is that some nodes, which overheard the information transmitted from the source node, relay it to the destination node instead of treating it as interference.

## Slide 6: Relay stretegy
Relaying done by:
amplify-and-forward: the relay nodes simply
boost the energy of the signal received from the
sender and retransmit it to the receiver.
In decode-and-forward, the relay nodes will perform decoding and then forward
the decoding result to the destinations.

## Slide 7: Transmission manner
three transmission manners in MANETs: direct transmissions (Fig. 1a), multihop
transmissions (Fig. 1b) and cooperative
transmissions (Fig. 1c).